## Slide 1: Probe Data Analysis for Road Slope
Zhiquan Li
Date: Mar/09/2018

## Slide 2: Outlines :
Background and Introduction
Problem Analysis
Algorithm Implementation
1.
2.
3.
4.
5.
Proposed Solution
Conclusions and Findings

## Slide 3: Background and Introduction
Nowadays, handled and dashboard-mounted travel guidance devices with embedded GPS have increased dramatically. The GPS trajectory collected by each device has been used in more and more applications, such as traffic flow analysis, geographical social network and so on.
However, the data of GPS trajectory is not precise since there are measure errors in devices and sampling.
Therefore, we need a method to map each GPS position with road network, then we could use these matched data to do further analysis

## Slide 4: Problem Analysis
The problem is divided into three parts, which are map-matching, road slope computation and result evaluation.
In map-matching, the GPS trajectory is collected by difference devices in different date, so the map-matching could be done in each device separately.
In slope computation and evaluation, we need to compute link slope with difference of altitude and distance between matched points and reference node, then we need to compare the deviation between the computed slope and the observed slope in the link data

## Slide 5: Proposed solution
In map-matching, we could match each GPS trajectory to its corresponding link by doing spatial analysis and temporal analysis, which is to find the highest possibility candidate point for each GPS trajectory in each link. The algorithm is introduced by a paper[1].
In slope computation and evaluation, we found each link would contain several matched points, so the link slope could be represented by the average slope of all matched points, then we could evaluate the result according the deviation between computed slope and observed slope.

## Slide 6
Algorithm Implementation: map-matching
In this step, we selected links within a radius of 20 meters of a GPS point. The reason we choose 20 meters is the paper[1] used a zero-mean normal distribution with standard deviation of 20 meters. Then, we could project a GPS point to each link to find candidate points
Step 1:
Candidate points for a sampling point 𝒑𝒊[1]

## Slide 7
Once we get candidate points for each GPS point, we start do spatial analysis, which is a multiplication of Observation probability and Transmission probability.
The Observation probability represent the likelihood of a candidate point is a matched point of GPS point according the distance between these points. The formula is show below:
where is the distance between . We use a zero-mean normal distribution with standard deviation of 20 meters.
Step 2:
Algorithm Implementation: map-matching

## Slide 8
The Transmission probability represent the likelihood of a path from to is the true path from to in the link. The formula is show below:
V
Where is the distance between and and is the shortest path from .
Then, we could do spatial analysis by using following formula:
V * ,
Step 2:
Algorithm Implementation: map-matching

## Slide 9
For distance computation of two points, we use Haversine formula:
Where is latitude, is longitude and r is the earth radius
Step 2:
Algorithm Implementation: map-matching
Spherical triangle solved by the law of haversines

## Slide 10
In this step, we need to do temporal analysis since it’s difficult to distinguish which road a GPS point should be belong to by spatial analysis if the GPS point in a parallel road. The formula is show below:
Where which is the average speed of the shortest path.
Step 3:
Algorithm Implementation: map-matching

## Slide 11
In this step, we compute ST function for each candidate point of each GPS point. The formula is showed below:
* ,
Then, we choose highest value of for each candidate point and record its parent point in a hash map. Once all candidates point have been computed, we could find the highest value of a candidate point in last GPS point would be the best path from to in the links, then we could find the matched point for each GPS point by tracing back according the parent hash map.
Step 4:
Algorithm Implementation: map-matching

## Slide 12
Result of sampleID 3496:
Algorithm Implementation: map-matching
Map-matching result of sampleID 3496

## Slide 13
Result of sampleID 3496:
Algorithm Implementation: map-matching
Matched points for probe points with sampleID 3496

## Slide 14
In slope computation and evaluation, we select matched points for each link and compute the average slope for all matched points from reference point. The formula is showed below:
Where is the ith matched point, is the altitude of ith matched point and refnode.alt is the altitude of reference node, n is the number of matched point in a link.
Then, we can do the evaluation part by computing the deviation between computed slope and observed slope by subtraction.
Algorithm Implementation: slope computation and evaluation

## Slide 15
The result is stored in a csv file in the same directory of the program after running the program. The feature in the file is linkID, computed slope, observed slope and deviation.
Part of result is showed below:
Algorithm Implementation: slope computation and evaluation
Result:
Example of result of slope computation and evaluation

## Slide 16
Conclusion and Findings
The ST Matching algorithm has good performance in map-matching, however, the algorithm is slow when dealing with huge amount of data since the time complexity is 𝑂(𝑛𝑘2𝑚 log 𝑚 + 𝑛𝑘2).
We may accelerate the processing speed by using distributed system

## Slide 17
Reference
1. Yin Lou, Chengyang Zhang, Yu Zheng, Xing Xie, Wei Wang, and Yan Huang, Map-Matching for Low-Sampling-Rate GPS Trajectories, Acm Sigspatial International Symposium on Advances in Geographic Information Systems, 2009 :352-361